## Slide 1: Computing Polynomials with Positive Coefficients Using Stochastic Logic by Double-NAND Expansion Sayed Ahmad Salehi, Yin Liu, Marc D. Riedel and Keshab K. Parhi
We compare the implementation of Example 1 in Fig. 4 and also polynomials related to Maclaurin series of , sec, and cosh based on the double-NAND method and other methods in Table 2 and Table 3.
Introduction
Department of Electrical and Computer Engineering
University of Minnesota Twin Cites, Minneapolis, MN
Stochastic Logic Circuits
Variables are represented by random bit-streams. Probability of seeing ‘1’ in the bit-stream determines the variable’s value.
Simple combinational logic gates can perform computations (Fig. 1).
Motivation (Goal):
The computation of polynomials of degree n, i.e.,
With all ’s are positive or zero and the sum of them is less than or equal to 1.
Key Contributions:
A novel extendable approach for implementation of polynomials with non negative coefficients using simple NAND and AND gates.
Methodology
In order to show that the circuit in Fig. 3 is valid, it is proven that all the coefficients in Fig. 3 are greater than 0 and less than 1.
Proof:
It is assumed that the sum of all ’s for is less than or equal to 1. Thus, the numerator and denominator of all the coefficients in Fig. 3 are greater than 0 meaning that these coefficients are greater than 0. All of the coefficients in Fig. 3 have the form of for . It is clear that for these coefficients the numerator is less than the denominator. Thus, the values of the coefficients are less than 1. □
1st and 2nd Order Polynomials:
First, consider the following simple example of the first-order polynomial:
.
For , ∈ [0,1), it can be mapped to the stochastic logic circuit shown in Fig. 2 (a).
Similarly, the second-order polynomial, , with all coefficients in the unit interval can be expressed as following and implemented as shown in Figure 2(b).
Experimental Results and Comparison
Conclusions
References
A new method called double_NAND expansion is presented for mapping certain class of polynomials to simple stochastic logic circuits.
The method can be generalized for a broader class of functions.
[1] Y.-N. Chang and K. K. Parhi. Architectures for digital filters using stochastic computing. IEEE ICASSP, pp. 2697–2701. IEEE, May 2013.
[2] W. Qian, X. Li, M. D. Riedel, K. Bazargan, and D. J. Lilja. An architecture for fault-tolerant computation with stochastic logic. IEEE Tran. on Comp., 60(1):93-105, 2011.
[3] Y. Liu and K. K. Parhi. Computing complex functions using factorization in unipolar stochastic logic. GVLSI, pp.109-112. ACM, 2016.
[4] P. Li, D. J. Lilja, W. Qian, K. Bazargan, and M. Riedel. The synthesis of complex arithmetic computation on stochastic bit streams using sequential logic. ICCCAD, pp. 480-487, 2012.
Acknowledgment
This work was supported by the National Science Foundation by grants CCF-1423407.
Fig. 2: Proposed circuits for computing (a) first-order polynomial
and (b) second-order polynomial.
(a)
(b)
Fig. 1: Stochastic logic units used in our proposed circuits: (a) AND computing z=xy, (b) NAND computing z=1-xy.
(a)
(b)
General Polynomials:
The approach can be extended for the general case of an eligible polynomial of degree , . First, can be written as follows:
Since has a form similar to the original the above mentioned step can be repeated for and the procedure
can be continued. This way, can be rewritten as
This equation can be mapped to the circuit shown in Fig. 3.
Fig. 3: General double-NAND structure for polynomial of degree .
TABLE 3:The mean absolute error (MAE) for computing polynomials in Example 1, , sec and cosh functions using the proposed method and previous methods.
Example 1:
The following example shows how double-NAND method can be used to implement by circuit of Fig. 4.
Fig. 4: Stochastic logic circuit for implementation
of polynomial .
Discussion
TABLE 2: The synthesis results for area in terms of two-input NAND gates and critical path (ns) for different stochastic logic polynomial and functions using 5 approaches.
[1]
[2]
[3]
[4]